## Slide 1
RTL TOOL OUTCOMES • KEV v1.0
What can KEV tell us
about an RTL design?
The tests, the completed Condor runs, and what the scores mean
Four model sizes • 151 retained designs • 725 held-out questions
15 October 2026
Notes: This presentation covers the completed KEV-0.8B, KEV-4B, KEV-9B and KEV-27B v1.0 runs. RTL means register-transfer level: code describing digital hardware. The label B denotes approximately billions of model parameters. There are 151 retained designs across development and test; the held-out test has 123 individual designs plus pair requests. The number 725 counts questions, not independent designs. All findings are specific to this dataset and tool flow. No Jev, base Qwen or commercial LLM evaluation is included.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 2
What the completed runs show
Different tasks reveal different strengths. A single pooled score hides important failures.
KEV v1.0 • Dataset v1 • 15 October 2026 | OVERVIEW
2
Better with 27B
Compilation errors:
8 of 9 detected
Area levels:
61 of 92 exactly right
Synthesis is weak
Synthesis failures:
4 of 24 detected
Failure reasons:
15 of 16 right when
failure is supplied
No single winner
9B leads area ranking.
27B leads power ranking.
Absolute power and
clock-frequency levels
remain unreliable.
All four runs completed. Every model answered every test question; missing data does not explain the errors.
Notes: The compilation-error result is KEV-27B on the 9 compiler-rejected test designs. The area result is 61/92 exact levels. Synthesis failure detection is 4/24. The 15/16 failure-reason result is conditional on a prompt explicitly stating that synthesis failed. The strongest observed pair-area accuracy is KEV-9B at 40/46 views; the strongest observed pair-power accuracy is KEV-27B at 31/44 views. These are different models and tasks, and not a single combined design or statistically established winner.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 3
Compilation and synthesis answer different questions
RTL = register-transfer level: source code that describes digital hardware.
KEV v1.0 • Dataset v1 • 15 October 2026 | TESTS
3
Does it compile?
Can the simulator compiler
accept the source code?
Reference: QuestaSim
vlog -sv.
This does not test whether
the circuit is correct.
Does it synthesize?
Can Design Compiler build
a complete gate-level
netlist from the code?
No unresolved modules.
All registers map to cells.
No synthesis errors.
What does it cost?
Estimate cell area, power,
and timing from the RTL.
The reference comes from
synthesis and power tools.
No fabricated-chip or
post-route measurement.
In the test set, 15 designs compile successfully but still fail synthesis.
Notes: Compilation uses Siemens QuestaSim 2022.4 vlog -sv, a compile-only check. Synthesis uses Synopsys Design Compiler U-2022.12-SP2 with analyze, elaborate, link and compile_ultra. A synthesis pass requires no Error lines, no LINK-5/UID-341 unresolved references, no TRANS-4 unmapped generic registers, and an output netlist. Compiler acceptance is not functional correctness, complete simulator elaboration, or a guarantee of synthesizability. There are 99 test designs with both successful compilation and synthesis, 15 that compile but fail synthesis, and 9 that fail both.
Evidence and reproducibility
notes/synth_yesno.md; notes/DATASET.md; harness/build.py; data/questions/dataset_v1.jsonl
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 4
The dataset and the held-out test set
One model request can contain several questions. Questions are not independent design samples.
KEV v1.0 • Dataset v1 • 15 October 2026 | TESTS
4
151
retained designs
348
requests across both splits
875
questions across both splits
Held-out request group | Requests | Questions | What is covered
Basic checks | 123 | 246 | Compilation + synthesis
Failure reason | 16 | 16 | One of ten reason options
Performance | 92 | 361 | Area, power and two timing levels
Pair comparisons | 50 | 102 | 25 distinct pairs, both orders
TOTAL TEST | 281 | 725 | 123 individual test designs
Development: 28 designs, 67 requests, 150 questions. Related base designs stay in the same split.
Notes: The plan ran 159 designs; 8 are excluded under the dataset rules, leaving 151 basic design records. The test split contains 123 basic designs and the development split 28. All four models answered all 348 requests, but reported accuracy uses test only: 281 requests and 725 questions. Performance coverage is 92 area, 92 slack, 92 reachable-frequency, and 85 power questions. The 361 performance questions therefore do not mean 361 distinct designs. There are 25 distinct test pairs, each sent in both orders, containing 46 area, 44 power and 12 frequency questions. Pair metrics overlap in which pairs they cover. The analysis asserts no shared base_design_id between development and test.
Evidence and reproducibility
notes/DATASET.md; data/questions/dataset_v1.card.md; data/questions/dataset_v1.jsonl; presentations/src/analyse_kev.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 5
What the model receives for each test
Tool logs and correct answers are used for scoring; they are not sent to the model.
KEV v1.0 • Dataset v1 • 15 October 2026 | TESTS
5
Basic checks
RTL source + top module + tool description.
Questions: does it compile, and does it synthesize?
Failure reason
The same source, plus a prompt saying synthesis failed.
Choose one reason from ten descriptions.
Performance
RTL + flow + clock target; power also gets its testbench.
Choose a level for each available metric.
Pair comparison
Both RTL variants + the same flow and clock.
Power comparisons also share the same testbench.
The failure-reason task supplies a key fact that the synthesis yes/no task must discover.
Notes: The Condor client sends only state, API model and questions to /v1/systemone. The correct_answer and evidence fields are retained locally in the input file and output records for scoring, not sent in the request payload. The four request groups are deliberately separate. In particular the reason instruction literally states that the tool does not synthesize the module, so its score cannot be read as autonomous failure detection. All models used the same input file SHA-256 and v1.0-tagged checkpoints. Maximum actual reported input length was 7,706 tokens for every model.
Evidence and reproducibility
condor/kev_client.py; harness/build.py: V1_QUESTIONS and build_dataset_v1; data/questions/dataset_v1.jsonl
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 6
How to read the scores
Every result needs a denominator and a clear rule for what counts as correct.
KEV v1.0 • Dataset v1 • 15 October 2026 | TESTS
6
Yes or no
A yes probability of
0.5 or more means yes.
Balanced accuracy gives
“yes” and “no” designs
equal weight.
Always one answer: 50%.
Five levels
Exact: the chosen level
matches the tool label.
Within one: a difference
of at most one level.
This does not mean a fixed
physical error tolerance.
Choose A or B
Each pair is sent twice,
with its order swapped.
We report per-view accuracy
and check both orders.
50% is an always-A or
always-B reference here.
A “constant-answer reference” below means always choosing one stated answer, calculated from test labels.
Notes: Binary predictions use threshold 0.5 exactly as the saved scorer. Class-specific rates use the actual tool outcome as the grouping variable. Binary balanced accuracy is the arithmetic mean of success recognition and failure detection. It equals the accuracy on a test set with equal numbers of “yes” and “no” designs, so always “yes” and always “no” both score 50% whatever the mix of the test set. The yes/no results slide shows this one score per model, with the answer mix of the model beside each bar. For reason labels the scorer averages per-class recall over the eight true classes present. Score probabilities use KEV keys 0 to 4, translated to displayed levels 1 to 5 before scoring. A constant-answer reference is a descriptive frequency of the specified label in this test set; it was not a separate run, not learned on development, and not chosen as a deployable predictor. Pair labels are exactly balanced A/B because both orders are included; always choosing a letter therefore gets 50%. There is no grand overall score across unrelated tasks.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 7
Only KEV-27B’s compilation score is far above 50%
One score per model: “yes” and “no” designs get equal weight. A constant answer scores 50%.
KEV v1.0 • Dataset v1 • 15 October 2026 | RESULTS
7
Does it synthesize?
Tool answers for the 123 designs: 99 yes · 24 no
0
50
100
0.8B
50.0%
123 yes · 0 no
4B
49.5%
122 yes · 1 no
9B
53.2%
119 yes · 4 no
27B
57.8%
118 yes · 5 no
Balanced accuracy (%) — higher is better
Dashed line: always “yes” or always “no” = 50%
Does it compile?
Tool answers for the 123 designs: 114 yes · 9 no
0
50
100
0.8B
51.8%
4 yes · 119 no
4B
50.0%
123 yes · 0 no
9B
61.1%
121 yes · 2 no
27B
94.4%
115 yes · 8 no
Balanced accuracy (%) — higher is better
Dashed line: always “yes” or always “no” = 50%
In the other seven cases, at least 118 of the 123 answers are the same.
Notes: One test set of 123 held-out designs answers both questions; all designs were sent together. Each bar is one score per model and question: balanced accuracy, the mean of the share of “yes” designs answered “yes” and the share of “no” designs answered “no”. It equals the accuracy on a test set with equal numbers of “yes” and “no” designs, so any constant answer scores exactly 50%. Plain accuracy over all 123 designs rewards a constant “yes”: always “yes” scores 80.5% for synthesis (99 of 123) and 92.7% for compilation (114 of 123). Beside each bar is the answer mix of the model (a yes probability of 0.5 or more counts as “yes”); compare it with the answer mix of the tool above the chart. Synthesis: “yes” designs answered “yes” 99, 98, 97, 98 of 99; “no” designs answered “no” 0, 0, 2, 4 of 24 (0.8B, 4B, 9B, 27B). Compilation: 4, 114, 114, 114 of 114 and 9, 0, 2, 8 of 9. With only 9 compile errors, one design changes the balanced score by 5.6 percentage points. KEV-0.8B answers “no” to compilation for 119 of the 123 designs, with yes probabilities between 0.30 and 0.53 for every design: its 9 of 9 on the compile errors is this near-constant “no”, not a detection. The question is yes/no only; it does not ask which error occurred (that is the failure-reason test, where 0.8B is right for 5 of 16). The same KEV-0.8B answers “yes” to synthesis for all 123 designs, so for 119 designs it answers both “does not compile” and “synthesizes”; in this test set, every design that vlog rejects also fails synthesis. The appendix slide “Most failing designs get the same answer as successes” shows every yes probability.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 8
Why 82.9% hid poor synthesis failure detection
KEV-27B • 123 held-out designs • a yes/no threshold of 0.5
KEV v1.0 • Dataset v1 • 15 October 2026 | RESULTS
8
Actual tool result | Model says YES | Model says NO
Synthesizes — 99 designs | 98 correct | 1 wrong
Fails synthesis — 24 designs | 20 wrong | 4 correct
82.9% overall accuracy
102 correct of 123 designs.
Each design has equal weight; the 99 successes dominate.
57.8% balanced accuracy
Average of 99.0% success recognition
and 16.7% failure detection. Each group gets half the weight.
20 failures
missed
Both percentages are correct. They answer different questions about an imbalanced test set.
Notes: KEV-27B confusion counts: true positive 98, false negative 1, false positive 20, true negative 4. Overall accuracy = (98+4)/123 = 0.8292682927. Success recognition = 98/99 = 0.9898989899. Failure detection = 4/24 = 0.1666666667. Balanced accuracy = (98/99+4/24)/2 = 0.5782828283. The always-yes descriptive reference is 99/123 = 80.5% overall and 50.0% balanced. The matrix contains actual counts, not probabilities. Never interpret overall 82.9% as 82.9% of failures detected.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 9
Which synthesis failures do the models detect?
Split the 24 failures again: source accepted by the simulator compiler versus rejected source.
KEV v1.0 • Dataset v1 • 15 October 2026 | RESULTS
9
Compiles, but fails synthesis
15 designs • synthesis-specific failure cases
0
50
100
0.8B
0.0%
0 of 15
4B
0.0%
0 of 15
9B
6.7%
1 of 15
27B
0.0%
0 of 15
Correct answers (%) — higher is better
Compilation also fails
9 designs • both tools reject the design
0
50
100
0.8B
0.0%
0 of 9
4B
0.0%
0 of 9
9B
11.1%
1 of 9
27B
44.4%
4 of 9
Correct answers (%) — higher is better
KEV-27B misses every one of the 15 synthesis failures whose source compiles.
Notes: This is a derived subgroup analysis using the actual compilation and synthesis labels of the same basic requests. All bars are synthesis yes/no decisions; the right panel is not the separate compilation answer. Compiler-accepted failure detections: 0,0,1,0 of 15. Compiler-rejected failure detections: 0,0,1,4 of 9. Small subgroups do not establish general performance, but clearly localise the observed weakness.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 10
Failure reasons: 27B gets 15 of 16 right
The prompt explicitly states that synthesis failed, then offers ten possible reasons.
KEV v1.0 • Dataset v1 • 15 October 2026 | RESULTS
10
Choose the correct failure reason
16 known-failure designs • one choice per design
0
50
100
0.8B
31.3%
5 of 16
4B
56.3%
9 of 16
9B
68.8%
11 of 16
27B
93.8%
15 of 16
Correct answers (%) — higher is better
What is measured
Can the model identify the reason
when failure is already known?
What the 27B error was
A multiple-driver error was labelled
as an asynchronous-reset error.
Only eight of the ten reason classes occur in these 16 test designs. Coverage is limited.
Notes: Correct reason counts are 5,9,11,15 of 16. Class-balanced reason accuracies are 17.9%,37.5%,50.0%,87.5%, respectively. The reason classes present are multiple_drivers(1), illegal_code(1), unsupported_construct(1), timing_control(3), simulation_statement(5), async_reset(1), mixed_assignments(2), instance_mismatch(2). There are no true event_list or unbounded_loop examples in the held-out reason subset. KEV-27B gets only multiple_drivers wrong, predicting async_reset. The instruction supplies the known failure and therefore this accuracy is conditional, not an end-to-end detection score.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 11
Diagnosing a known failure is not detecting that failure
Match the two saved responses for the same 16 reason-test designs.
KEV v1.0 • Dataset v1 • 15 October 2026 | RESULTS
11
Model | Says synthesis failed | Correct reason when told it failed | Both answers correct
KEV-0.8B | 0 of 16 | 5 of 16 | 0 of 16
KEV-4B | 0 of 16 | 9 of 16 | 0 of 16
KEV-9B | 1 of 16 | 11 of 16 | 1 of 16
KEV-27B | 0 of 16 | 15 of 16 | 0 of 16
27B: 15 correct diagnoses, but zero failure flags on these same designs.
This is a linked analysis of existing answers, not a separately run detection-and-diagnosis system.
Notes: For each test reason request, replace :reason: with :basic: in its question ID and inspect the corresponding synthesis probability. The reason subset has 16 known failures, while the full binary synthesis test has 24 failures; 8 noncompile designs do not receive a reason request. Failure flags within the 16-design reason subset are 0,0,1,0. Correct diagnoses when the prompt supplies failure are 5,9,11,15. Both correct counts are 0,0,1,0. In particular KEV-27B flags none of these 16, although its independent reason response is right for 15. These are retrospective conjunctions of saved answers, not measured performance of a deployed routed pipeline.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 12
Area and power: choose one of five ranges
The model estimates a level from source code and flow information, not an exact physical value.
KEV v1.0 • Dataset v1 • 15 October 2026 | TESTS
12
Metric | Level 1 | Level 2 | Level 3 | Level 4 | Level 5
Cell area (gate equivalents) | <100 | 100 to <1,000 | 1,000 to <10,000 | 10,000 to <100,000 | ≥100,000
Total power (microwatts) | <10 | 10 to <100 | 100 to <1,000 | 1,000 to <10,000 | ≥10,000
Area reference
1 gate equivalent = one two-input NAND gate
= 0.196608 square micrometres in this library.
Power reference
Dynamic + leakage, for the supplied stimulus.
1,000 microwatts = 1 milliwatt.
Exact level is strict; “within one level” can span a large physical range because these bins are logarithmic.
Notes: The reference synthesis uses the supplied RTL_flow_Nangate15, NanGate 15nm typical corner at 0.8 V and 25 C, Design Compiler compile_ultra -gate_clock, a 500 MHz target, input/output delay of 10% of period, and 50 ps setup clock uncertainty. Area is the synthesis total cell area divided by 0.196608 square micrometres per NAND2_X1 gate. Power comes from the same design run and PrimeTime total dynamic plus leakage power using its supplied power testbench. The model receives that testbench. Power is only included when the run is successful and switching annotation is at least 95%. In the held-out test 85 of 92 performance requests have a power label; the other seven are excluded, not model errors. Levels use lower-inclusive upper-exclusive ranges, except the first and last open-ended bins.
Evidence and reproducibility
harness/build.py: AREA_EDGES_GE, POWER_EDGES_UW and build_dataset_v1; notes/DATASET.md; notes/README.md
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 13
Timing: margin at 500 MHz, plus a derived frequency
The clock target is 500 MHz: one cycle lasts 2 nanoseconds (ns).
KEV v1.0 • Dataset v1 • 15 October 2026 | TESTS
13
Metric | Level 1 | Level 2 | Level 3 | Level 4 | Level 5
Worst slack (timing margin) | Negative: misses target | 0 to <0.5 ns | 0.5 to <1.0 ns | 1.0 to <1.5 ns | ≥1.5 ns
Reachable clock frequency | <1 GHz | 1 to <2 GHz | 2 to <3 GHz | 3 to <4 GHz | ≥4 GHz
Reachable frequency (GHz) = 1 ÷ [2 ns − worst slack (ns)]
Example: 1.438 ns of slack gives a 0.562 ns limiting delay, or about 1.78 GHz.
This is derived from the netlist synthesized at 500 MHz; it is not a new optimized run.
No negative-slack designs occur in this test split. Timing-violation detection is therefore not evaluated.
Notes: Worst slack is the smallest timing margin reported after synthesis at the fixed 500 MHz target. Positive slack means the netlist meets that target. Reachable frequency is the harness formula 1000/(period_ns-slack_ns) MHz, converted here to GHz, from that same netlist. It is not measured silicon frequency, post-route timing or the result of resynthesizing at the inferred faster target. The example mac_int8 has 1437.97 ps of slack, converted to 1.43797 ns: 1/(2-1.43797)=1.779 GHz. A unit conversion bug in the supplied summary.sh is corrected by the harness. Held-out slack truths contain levels 2,3,4,5 only; reachable frequency truths contain levels 1,2,3,4 only. Thus no negative-slack or ≥4 GHz true examples occur.
Evidence and reproducibility
notes/DATASET.md; harness/build.py: SLACK_EDGES_NS, REACH_EDGES_MHZ and build_dataset_v1; flow/RTL_flow_Nangate15/summary.sh
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 14
Area levels improve substantially with 9B and 27B
92 held-out designs • same flow and target • exact and within-one scores shown separately.
KEV v1.0 • Dataset v1 • 15 October 2026 | RESULTS
14
Exact area level
All five true area levels occur
0
50
100
0.8B
35.9%
33 of 92
4B
35.9%
33 of 92
9B
57.6%
53 of 92
27B
66.3%
61 of 92
Correct answers (%) — higher is better
Dashed line: always level 1 = 35.9%
Within one area level
Chosen level differs by at most one
0
50
100
0.8B
66.3%
61 of 92
4B
70.7%
65 of 92
9B
90.2%
83 of 92
27B
100.0%
92 of 92
Correct answers (%) — higher is better
27B: 61 of 92 exact levels; all 92 estimates are within one level.
Notes: Exact area hits: 33,33,53,61 of 92. Within-one hits: 61,65,83,92. The dashed constant-answer reference is always area level 1, correct for 33/92 test examples. It is descriptive and computed from test labels, not an independently run or development-selected model. Even a within-one prediction can imply a large area difference because the bins have decade-wide boundaries. No physical relative error or post-layout area is reported.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 15
Power levels: the largest model performs worst
85 held-out designs with usable power measurements and a supplied stimulus testbench.
KEV v1.0 • Dataset v1 • 15 October 2026 | RESULTS
15
Exact power level
Levels 1 to 4 occur; level 5 is absent
0
50
100
0.8B
27.1%
23 of 85
4B
45.9%
39 of 85
9B
40.0%
34 of 85
27B
10.6%
9 of 85
Correct answers (%) — higher is better
Dashed line: always level 2 = 43.5%
Within one power level
Chosen level differs by at most one
0
50
100
0.8B
82.4%
70 of 85
4B
91.8%
78 of 85
9B
92.9%
79 of 85
27B
64.7%
55 of 85
Correct answers (%) — higher is better
27B predicts only levels 3–5, although 60 of the 85 true labels are levels 1–2.
Notes: Exact power hits: 23,39,34,9 of 85. Within-one hits: 70,78,79,55. True level counts 1–5: 23,37,18,7,0. KEV-27B chosen-level counts: 0,0,54,30,1. It therefore systematically chooses high levels on this test distribution. This is an observed tendency, not evidence of an identified root cause. Power depends on both the synthesized design and stimulus; it is not a general intrinsic cost of the RTL. The constant-answer level-2 reference is computed from test labels.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 16
Timing levels remain unreliable for every model
92 held-out designs • these are level estimates from RTL, not timing-tool replacements.
KEV v1.0 • Dataset v1 • 15 October 2026 | RESULTS
16
Exact clock-frequency level
Frequency derived from the 500 MHz netlist
0
50
100
0.8B
14.1%
13 of 92
4B
12.0%
11 of 92
9B
14.1%
13 of 92
27B
14.1%
13 of 92
Correct answers (%) — higher is better
Dashed line: always level 4 = 48.9%
Exact timing-margin level
Worst slack at the 500 MHz target
0
50
100
0.8B
8.7%
8 of 92
4B
4.3%
4 of 92
9B
3.3%
3 of 92
27B
32.6%
30 of 92
Correct answers (%) — higher is better
Dashed line: always level 5 = 68.5%
27B’s better slack result still falls below the stated constant-answer reference.
Notes: Reachable frequency exact hits are 13,11,13,13 of 92. Slack exact hits are 8,4,3,30 of 92. True frequency level 4 is most common with 45/92 and true slack level 5 with 63/92. These are explicitly specified constant-answer references calculated from the test labels, not learned predictive baselines. No negative-slack cases are present, so the benchmark cannot evaluate missed timing violations. Level accuracy is not a timing estimation error in picoseconds or MHz.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 17
27B’s predicted levels reveal the mismatch
The chart heights are design counts, not accuracy. Every level is shown, including zero counts.
KEV v1.0 • Dataset v1 • 15 October 2026 | RESULTS
17
Clock-frequency levels
92 designs • counts at each level
0
25
50
75
100
13
90
1
16
0
2
18
0
3
45
0
4
0
2
5
Level (1–5)
Tool
27B
Power levels
85 designs • counts at each level
0
25
50
75
100
23
0
1
37
0
2
18
54
3
7
30
4
0
1
5
Level (1–5)
Tool
27B
27B usually chooses the lowest frequency level and high power levels; the tool labels have a different distribution.
Notes: These are the complete true-label and chosen-label distributions for KEV-27B test performance responses. Frequency truths 13,16,18,45,0 and predictions 90,0,0,0,2. Power truths 23,37,18,7,0 and predictions 0,0,54,30,1. Each chart uses the same 0–100-design vertical scale; the two denominators are different and labelled. There is no omission or zoom. Counts at zero are printed as zero rather than represented by a nonzero bar. These distributions establish bias in chosen levels, not its cause.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 18
Pair tests ask which variant is better
Two candidates for the same problem, with the same flow and power stimulus.
KEV v1.0 • Dataset v1 • 15 October 2026 | TESTS
18
Three comparisons
Smaller cell area
Lower total power
Higher derived clock frequency
Eligibility and coverage
Metric differs by at least 10%.
Area: 23 distinct pairs, 46 views.
Power: 22 pairs, 44 views.
Frequency: 6 pairs, 12 views.
First request: [design X = A] [design Y = B]
Swap request: [design Y = A] [design X = B]
A model tracking the better design should switch letters when the design order is swapped.
Notes: Pair inputs are old REvolution candidates of the same problem. Both runs must have usable power and at least 95% annotation, the same power testbench, and positive values for compared metrics. A question is retained for a metric if max/min is at least 1.1, so there are no ties. Twenty-five distinct pairs occur in the held-out split and 31 across both splits. The metric subsets overlap; do not sum 23+22+6 as distinct pairs. Each retained pair is sent as AB and BA. A/B labels are therefore balanced. No energy-per-operation pair question is implemented in dataset v1, despite its presence in an older planning note.
Evidence and reproducibility
harness/build.py: V1_PAIR_QUESTIONS and build_dataset_v1; data/questions/dataset_v1.jsonl; notes/DATASET.md
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 19
Pair rankings improve, but the strongest model varies
Per-view accuracy: each distinct pair contributes its two presentation orders.
KEV v1.0 • Dataset v1 • 15 October 2026 | RESULTS
19
Choose the smaller area
23 distinct pairs • 46 views
0
50
100
0.8B
47.8%
22 of 46
4B
76.1%
35 of 46
9B
87.0%
40 of 46
27B
78.3%
36 of 46
Correct answers (%) — higher is better
Dashed line: always A or B = 50%
Choose lower power
22 distinct pairs • 44 views
0
50
100
0.8B
63.6%
28 of 44
4B
56.8%
25 of 44
9B
65.9%
29 of 44
27B
70.5%
31 of 44
Correct answers (%) — higher is better
Dashed line: always A or B = 50%
Choose higher frequency
6 distinct pairs • 12 views
0
50
100
0.8B
66.7%
8 of 12
4B
83.3%
10 of 12
9B
75.0%
9 of 12
27B
83.3%
10 of 12
Correct answers (%) — higher is better
Dashed line: always A or B = 50%
9B leads area ranking (40 of 46 views); 27B leads power ranking (31 of 44). Frequency has only six pairs.
Notes: The full pair accuracy values are taken from the official local harness scorer. Per-view hits: area 22,35,40,36 of 46; power 28,25,29,31 of 44; frequency 8,10,9,10 of 12. The dashed 50% reference is always choosing A or always choosing B because both orders are included. This is not independent random sampling: the two orders share designs, and different pairs can share candidates of a problem. No significance test is claimed, and different per-task maxima belong to different models. All percentage axes are 0–100%.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 20
Check the design ranking in both orders
A stronger test counts a pair correct only when both presentation orders are correct.
KEV v1.0 • Dataset v1 • 15 October 2026 | RESULTS
20
Model | Area: both correct 23 pairs | Power: both correct 22 pairs | Frequency: both correct 6 pairs
KEV-0.8B | 5 of 23 | 6 of 22 | 3 of 6
KEV-4B | 13 of 23 | 3 of 22 | 4 of 6
KEV-9B | 19 of 23 | 9 of 22 | 4 of 6
KEV-27B | 17 of 23 | 14 of 22 | 5 of 6
Same letter after swapping the power pair:
0.8B: 16 of 22 pairs • 4B: 19 of 22 • 9B: 11 of 22 • 27B: 3 of 22
Keeping the same letter after a swap guarantees at least one wrong view. Lower is better for that error count.
Notes: Both-order correct counts are derived from matching AB/BA answers and requiring each to equal its label. Area:5,13,19,17 of23; power:6,3,9,14 of22; frequency:3,4,4,5 of6. Same-letter-both-orders is the saved scorer positional inconsistency measure; power counts are16,19,11,3 of22. A consistent switched-letter answer can still choose the wrong design in both orders, so consistency alone does not prove correctness. The both-orders criterion is therefore shown separately from the per-view accuracy. It is a stricter descriptive summary, not a new experiment.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 21
All four Condor evaluations completed
Observed run times include different hardware and setup costs; they are not a controlled speed ranking.
KEV v1.0 • Dataset v1 • 15 October 2026 | EXECUTION
21
Model | Job | GPU used | Job time including setup | Median model time per request
KEV-0.8B | 4.0 | RTX 3080 Ti | 125 s | 109 ms
KEV-4B | 5.0 | A100 80 GB | 187 s | 201 ms
KEV-9B | 6.0 | A100 80 GB | 204 s | 244 ms
KEV-27B | 7.0 | A100 80 GB | 400 s | 668 ms
Every model: 348 dataset requests answered, 5 smoke requests passed,
725 test questions scored, zero HTTP errors and zero missing answers.
All runs used the same dataset fingerprint and v1.0 checkpoints. Maximum reported input length: 7,706 tokens.
Notes: Condor job IDs4.0,5.0,6.0,7.0 completed with return code0. Job execution seconds are125,187,204,400; this includes setup/smoke/inference but excludes idle queue wait. Median server-reported model times are109.05,201.35,243.7,668.3ms. These medians include all348 dataset requests, development plus test, but exclude the separate smoke file. GPU0.8B: euler RTX3080Ti; larger models: aristoteles A100-SXM4-80GB. Sum of client wall times over the348 requests:52.047,99.433,104.114,279.849s. Server model latency and client wall time are distinct measures. Peak sampled GPU memory is recorded for0.8B only (7036MiB); no comparable peak is available for the larger jobs. An earlier0.8B attempt3.0 failed before inference on AMD and was corrected by requiring CUDA. No dollar-cost estimate is measured.
Evidence and reproducibility
results/kev/*/manifest.json; condor/logs/4.0.kev-0.8b.log; condor/logs/5.0.kev-4b.log; condor/logs/6.0.kev-9b.log; condor/logs/7.0.kev-27b.log
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 22
What the evidence supports—and what needs work
These are observations on dataset v1, not a guarantee for unseen design families.
KEV v1.0 • Dataset v1 • 15 October 2026 | INTERPRETATION
22
Promising in this test
27B: source-compilation screening.
27B: failure reasons when failure is known.
27B: coarse area levels.
9B: pairwise area ranking.
27B: pairwise power ranking.
Next experiments
Choose binary thresholds on development data.
Expand synthesis failures and rare classes.
Add designs that miss the timing target.
Check power and timing across design groups.
Compare other models under the same protocol.
Keep tool verification in the loop. Reliable synthesis-failure screening is not established by these scores.
Notes: This slide distinguishes measured strengths from proposed follow-up work. The test-set probabilities suggest that the fixed0.5 threshold may hide some ranking signal, but any alternative threshold must be selected on development only, frozen and assessed on new held-out data rather than optimised on this test. Expanded failure cases should include compiler-accepted synthesis failures. The current test has no negative-slack cases, no level5 power examples, and no level5 reachable-frequency examples. No confidence interval or paired significance test is claimed here. Jev, base Qwen, commercial LLMs, renamed/comment controls, energy per operation and post-route or measured-silicon validation have no results in this completed evaluation.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 23
THE DETAIL BEHIND THE NUMBERS
Full results and
coverage limits
Exact counts, probability metrics, level errors and reproducible evidence
Notes: Appendix for review and reproduction. The following tables retain all primary question metrics, the class splits, reason coverage, probability metrics, expected-level error and pair-order checks. There is no single overall cross-task accuracy because tasks have different meanings, supports and class distributions.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 24
Every primary test score
Correct answers (%) • each question has equal weight within its row • higher is better.
KEV v1.0 • Dataset v1 • 15 October 2026 | APPENDIX
24
Task | Questions | 0.8B | 4B | 9B | 27B
Compiles — pooled | 123 | 10.6% | 92.7% | 94.3% | 99.2%
Synthesizes — pooled | 123 | 80.5% | 79.7% | 80.5% | 82.9%
Failure reason — known failure | 16 | 31.3% | 56.3% | 68.8% | 93.8%
Area — exact level | 92 | 35.9% | 35.9% | 57.6% | 66.3%
Power — exact level | 85 | 27.1% | 45.9% | 40.0% | 10.6%
Clock frequency — exact level | 92 | 14.1% | 12.0% | 14.1% | 14.1%
Timing margin — exact level | 92 | 8.7% | 4.3% | 3.3% | 32.6%
Pair: smaller area | 46 | 47.8% | 76.1% | 87.0% | 78.3%
Pair: lower power | 44 | 63.6% | 56.8% | 65.9% | 70.5%
Pair: higher frequency | 12 | 66.7% | 83.3% | 75.0% | 83.3%
Pooled yes/no scores conceal class imbalance. Use the successful/failing split on the next slide.
Notes: This is the complete primary accuracy table from the saved scorer, reproduced from raw answers. The KEV model size is indicated by the four numeric columns; all are KEV v1.0. Yes/no scores use threshold0.5. Reason accuracy is conditional on the prompt supplying failure. Area/power/frequency/slack require exact ordinal level. Pair scores count both presentation orders as separate views; area46views, power44views, frequency12views. No row is a general combined model score. For probability, class and level-error metrics see later appendix slides.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 25
Yes/no checks: every class, count and weighting
“Correct” below is measured within the actual tool-outcome group.
KEV v1.0 • Dataset v1 • 15 October 2026 | APPENDIX
25
Actual tool group | Designs | 0.8B | 4B | 9B | 27B
Compilation: successes | 114 | 4 (3.5%) | 114 (100.0%) | 114 (100.0%) | 114 (100.0%)
Compilation: failures | 9 | 9 (100.0%) | 0 (0.0%) | 2 (22.2%) | 8 (88.9%)
Compilation: balanced | — | 51.8% | 50.0% | 61.1% | 94.4%
Compilation: “yes” answers | 123 | 4 | 123 | 121 | 115
Synthesis: successes | 99 | 99 (100.0%) | 98 (99.0%) | 97 (98.0%) | 98 (99.0%)
Synthesis: failures | 24 | 0 (0.0%) | 0 (0.0%) | 2 (8.3%) | 4 (16.7%)
Synthesis: balanced | — | 50.0% | 49.5% | 53.2% | 57.8%
Synthesis: “yes” answers | 123 | 123 | 122 | 119 | 118
Group rows: number correct, then the percentage of that group. “Yes” rows count all 123 designs.
Balanced accuracy averages success recognition and failure detection with 50% weight each.
Notes: The rows show all four binary confusion-matrix supports with correct counts. Wrong counts are n minus correct. Compilation supports114pass/9fail; synthesis99pass/24fail. Balanced accuracy is the arithmetic mean of the two within-group percentages, not weighted by123designs. KEV0.8B synthesis always predicts yes. KEV4B compilation always predicts yes. The source answers are all present and successfully scored; there is no missing-answer adjustment. The “yes” rows count the answers with a yes probability of 0.5 or more among all 123 test designs: correct answers on successes plus wrong answers on failures.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 26
Most failing designs get the same answer as successes
Each dot is one held-out design. A yes probability of 0.5 or more counts as “yes”.
KEV v1.0 • Dataset v1 • 15 October 2026 | APPENDIX
26
Does it synthesize?
● tool synthesizes: 99 ● tool fails: 24
0
0.5
1
0.8B
123 of 123
are “yes”
4B
122 of 123
are “yes”
9B
119 of 123
are “yes”
27B
118 of 123
are “yes”
Yes probability of each design • dashed line: 0.5 threshold
Does it compile?
● vlog accepts: 114 ● vlog rejects: 9
0
0.5
1
0.8B
4 of 123
are “yes”
4B
123 of 123
are “yes”
9B
121 of 123
are “yes”
27B
115 of 123
are “yes”
Yes probability of each design • dashed line: 0.5 threshold
Only KEV-27B’s compile answers are right in both groups: 114 of 114 and 8 of 9.
Notes: Each dot is the saved noul answer (the yes probability) of one held-out basic request. In each model row, the upper teal dots are the designs that the tool accepts and the lower orange dots are the designs that the tool rejects. The small vertical spread in each lane comes from a fixed hash of the question ID and only reduces overlap; it carries no data. A probability of 0.5 or more counts as “yes”, as in the saved scorer. “Yes” answers of 123, synthesis: 123, 122, 119, 118; compilation: 4, 123, 121, 115 (0.8B, 4B, 9B, 27B). KEV-0.8B gives every design a compile probability between 0.30 and 0.53 and a synthesis probability between 0.52 and 0.74, for successes and failures alike (AUROC 0.563 and 0.490; 0.5 is chance). KEV-27B compile probabilities: successes 0.56 to 0.99, failures 0.24 to 0.68 (AUROC 0.994). KEV-27B synthesis probabilities: the 9 failures that also fail vlog rank below the successes (AUROC 0.982), but only 4 fall below 0.5; the 15 failures that pass vlog get 0.60 to 0.95 (AUROC 0.713). The Kev README names no RTL training data. A search of the Kev suites (evals/) for Verilog terms finds only the C++ logging macro VLOG and the word “vlog” in a text about videos. Kev-27B also trained on C++ code-review questions (devtools-v1) and starts from a post-trained Qwen model whose training data is not published.
Evidence and reproducibility
results/kev/*/dataset_v1__*.jsonl; presentations/src/analyse_kev.py; github.com/jaredpalmer/kev README and evals/ (commit 5e42a7a)
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 27
Failure-reason coverage is small and uneven
Correct reason counts by actual class • the prompt supplies that failure occurred.
KEV v1.0 • Dataset v1 • 15 October 2026 | APPENDIX
27
Actual failure class | Cases | 0.8B | 4B | 9B | 27B
More than one driver | 1 | 0 | 0 | 0 | 0
Illegal code | 1 | 0 | 0 | 0 | 1
Unsupported construct | 1 | 0 | 1 | 1 | 1
Unsupported timing control | 3 | 1 | 3 | 3 | 3
Simulation-only statement | 5 | 3 | 5 | 5 | 5
Asynchronous reset | 1 | 0 | 0 | 0 | 1
Mixed assignment styles | 2 | 0 | 0 | 0 | 2
Module-instance mismatch | 2 | 1 | 0 | 2 | 2
Equal weight per observed class | Accuracy | 17.9% | 37.5% | 50.0% | 87.5%
No true event-list or unbounded-loop cases occur in this held-out subset.
These two offered classes therefore have no measured class recall.
Notes: The eight observed reason classes and supports are drawn from the test input. They total16. The offered option list has10classes, so event_list and unbounded_loop have zero true cases and are excluded from the saved scorer balanced accuracy. Correct class counts for every model are recomputed. KEV27B sole mistake is multiple_drivers→async_reset. Five simulation-only examples and three timing-control examples give those classes more influence in pooled accuracy than one-case classes. Balanced accuracy instead weights the eight observed class recalls equally. Do not interpret this as broad10-class validation.
Evidence and reproducibility
notes/synth_reason.md; data/questions/dataset_v1.jsonl; presentations/data/verified_metrics.json
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 28
Probability ranking and binary decisions are different
A model can rank cases reasonably while making poor decisions at the fixed 0.5 threshold.
KEV v1.0 • Dataset v1 • 15 October 2026 | APPENDIX
28
Probability metric | 0.8B | 4B | 9B | 27B
Compilation: ranking score (AUROC) | 0.563 | 0.763 | 0.692 | 0.994
Compilation: probability error (Brier) | 0.334 | 0.064 | 0.066 | 0.030
Synthesis: ranking score (AUROC) | 0.490 | 0.714 | 0.740 | 0.814
Synthesis: probability error (Brier) | 0.187 | 0.148 | 0.144 | 0.128
Ranking score: higher is better
Chance = 0.5; perfect ordering = 1.
Compares yes probabilities for successes and failures.
Probability error: lower is better
Mean squared error of the yes probability.
Zero is perfect; confidently wrong answers cost more.
Notes: AUROC is the probability that a randomly chosen actual success has a higher predicted yes probability than a randomly chosen actual failure, counting ties as half. It ranges0–1;0.5 corresponds to chance ordering. It is independent of the chosen decision threshold and is not failure recall. Brier score is mean((p_yes-y)^2),0–1with lower better. It measures probability error, not calibration alone. These metrics use all123binary test designs. Synthesis AUROC improves to0.814for27B although its thresholded failure recall is16.7%. Any threshold tuning must use the development split, not these test labels. No recalibrated or alternative-threshold result has been run.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 29
Performance levels: tolerance and expected-level error
Within one level: higher is better. Mean level error: lower is better.
KEV v1.0 • Dataset v1 • 15 October 2026 | APPENDIX
29
Metric | Measure | 0.8B | 4B | 9B | 27B
Area | Within one level | 66.3% | 70.7% | 90.2% | 100.0%
Area | Mean level error | 0.994 | 0.713 | 0.649 | 0.485
Power | Within one level | 82.4% | 91.8% | 92.9% | 64.7%
Power | Mean level error | 0.971 | 0.754 | 0.900 | 1.070
Clock frequency | Within one level | 31.5% | 31.5% | 33.7% | 31.5%
Clock frequency | Mean level error | 1.119 | 1.321 | 1.208 | 1.242
Timing margin | Within one level | 30.4% | 28.3% | 12.0% | 40.2%
Timing margin | Mean level error | 1.509 | 1.654 | 1.742 | 1.622
Mean level error uses the probability-weighted expected level, not just the most likely level.
Unequal physical bin widths mean that one level is not a fixed physical error.
Notes: The saved scorer computes within_one from the argmax chosen level versus the true integer level. Mean absolute level error (mae_levels) uses the probability-weighted expected level sum(k*p_k)/sum(p_k), then averages abs(expected-true). Therefore it is not the mean absolute error of the argmax level and need not track exact accuracy monotonically. Supports:92area,85power,92reachablefrequency,92slack. Since area and power bins cover decades, ordinal error cannot be read as fixed relative or absolute physical error. All values are retained from the scorer, verified against raw responses with1e-12floating-point tolerance.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 30
Pair order: all correctness and letter-bias counts
Counts are per distinct pair. Each pair has exactly two model answers.
KEV v1.0 • Dataset v1 • 15 October 2026 | APPENDIX
30
Pair outcome | Pairs | 0.8B | 4B | 9B | 27B
Area — Both orders correct | 23 | 5 | 13 | 19 | 17
Area — One order correct | 23 | 12 | 9 | 2 | 2
Area — Neither order correct | 23 | 6 | 1 | 2 | 4
Power — Both orders correct | 22 | 6 | 3 | 9 | 14
Power — One order correct | 22 | 16 | 19 | 11 | 3
Power — Neither order correct | 22 | 0 | 0 | 2 | 5
Frequency — Both orders correct | 6 | 3 | 4 | 4 | 5
Frequency — One order correct | 6 | 2 | 2 | 1 | 0
Frequency — Neither order correct | 6 | 1 | 0 | 1 | 1
With two opposite correct letters, “one order correct” is the same as keeping the same letter.
A consistent letter swap can still be wrong in both orders.
Notes: For an A/B pair with opposite correct labels in AB and BA, each model response falls into0,1or2correct views. Both-order counts are read from paired saved answers, not estimated from percentages. The saved same_letter_both_orders rate equals the one-correct count divided by the number of distinct pairs for this balanced binary protocol. It is not itself an accuracy measure. Questions share design candidates and problem families, so naive independence across views is inappropriate. All row triplets sum to the labelled number of pairs.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 31
Dataset composition and missing coverage
The retained designs cover several sources; this is not a balanced population sample.
KEV v1.0 • Dataset v1 • 15 October 2026 | APPENDIX
31
Design group | All retained | Held-out designs | Held-out synthesis failures
MetRex: varied sizes | 40 | 31 | 0
Injected synthesis errors | 16 | 9 | 9
Natural language-model candidates | 20 | 17 | 0
Injected compilation errors | 8 | 8 | 8
Human reference designs | 15 | 11 | 0
Older REvolution candidates | 32 | 28 | 1
REvolution v0 designs | 10 | 9 | 0
Accepted edits and rejected twins | 10 | 10 | 6
Not measured here: energy per operation, functional equivalence, post-route timing,
measured chips, other model families, or the older plan’s rename/comment controls.
Notes: The group counts are based on retained basic design records only, not requests or pair views. All retained counts total151 and held-out counts123. The original plan159had8excludeddesigns:4mutantswithanunintendedclass,2traptwins that did not synthesize as required, and2noncompile designs whose DC class was not intended. Twelve retained performance cases across both splits have no usable power value, leaving98powerquestions overall and85test. The corpus also skips comparisons with incompatible testbenches or less than10%metric differences. Some source groups contain near variants; base_design_id grouping prevents cross-split leakage as checked in analyse_kev.py. Dataset v1 supersedes older planning sizes such as500perquestiontype. No planned result is presented as completed.
Evidence and reproducibility
data/questions/dataset_v1.card.md; notes/DATASET.md; harness/build.py; presentations/data/verified_metrics.json
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.

## Slide 32
Evidence needed to reproduce this deck
Every number is tied to the frozen dataset and saved responses; no model reruns were needed.
KEV v1.0 • Dataset v1 • 15 October 2026 | APPENDIX
32
Model | Condor job | Completed on 15 October | Checkpoint revision (prefix)
KEV-0.8B | 4.0 | 11:30:55 | bf75a6a8848e
KEV-4B | 5.0 | 14:31:45 | 6cfce5c2fa4b
KEV-9B | 6.0 | 14:34:55 | db029f08b290
KEV-27B | 7.0 | 14:39:12 | af0e6d551bdc
Inputs and evidence
Questions: data/questions/dataset_v1.jsonl
Answers, scores and manifests: results/kev/
Verified tables and rebuild scripts: presentations/data/ and presentations/src/
Notes: Full provenance:
{
"kev-0.8b": {
"job": "4.0",
"revision": "bf75a6a8848ea6960ff2ed108d9ed44c2941174f",
"answers_file": "results/kev/dataset_v1_kev-0.8b_20261014/dataset_v1__kev-0.8b.jsonl",
"answers_sha256": "c2b175aacc788e57d7b3fbc042432c9d3fac78384ae37bc976f8bf52d9c22046",
"dataset_sha256": "96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a"
},
"kev-4b": {
"job": "5.0",
"revision": "6cfce5c2fa4b4bd64026336ab649c5ca78857d52",
"answers_file": "results/kev/dataset_v1_kev-4b_20261015/dataset_v1__kev-4b.jsonl",
"answers_sha256": "9f68340c80d407377a5288c970bab9a1af2a203aa6128c56a80555dece270b6e",
"dataset_sha256": "96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a"
},
"kev-9b": {
"job": "6.0",
"revision": "db029f08b290afd9fee4aa4bbcd9ae48602d1eb0",
"answers_file": "results/kev/dataset_v1_kev-9b_20261015/dataset_v1__kev-9b.jsonl",
"answers_sha256": "5c69346a7c9211caaff5f0e6067e82a5f6022519029d5cd1634697a1710fde34",
"dataset_sha256": "96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a"
},
"kev-27b": {
"job": "7.0",
"revision": "af0e6d551bdc2cc724f3e9d7a8bee1cd4fb8f7bf",
"answers_file": "results/kev/dataset_v1_kev-27b_20261015/dataset_v1__kev-27b.jsonl",
"answers_sha256": "c643020e0b73e9627c81fb7b0429556c70969cfef7074b7e4f6fc71d1349bf19",
"dataset_sha256": "96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a"
}
}
All times are Europe/Paris (CEST) as recorded in the manifests. The build verifies unique request IDs, successful HTTP responses, matching question keys, no cross-split base IDs, input fingerprints, and saved metrics versus freshly recomputed metrics. Numerical floating-point differences up to1e-12are accepted. Theme and slide masters are inherited from the user-supplied reference. This deck is derived from the completed results only.
Evidence and reproducibility
data/questions/dataset_v1.jsonl; results/kev/*/dataset_v1__*.jsonl; harness/score.py
All numerical results use the held-out test split unless explicitly labelled otherwise.
Dataset SHA-256: 96814ea63d89b98af7f87c5f6d8e5fe0f35ec710c30755c9d0723fbec4ddbe2a
Verified calculations: presentations/data/verified_metrics.json.
Rebuild: python3 presentations/src/build_kev_findings.py.
Visual style: pwp_example/TinyTapeOut 2026 jullie feedback.pptx; original theme and slide masters retained.
All charts, diagrams and tables on this slide are editable PowerPoint objects.